## Slide 1: 封面
Version:20240424
Introduce of Hongmei Power
Semiconductor specialty products

## Slide 2
One station/Cost-effective solution supplier of power semiconductor devices

## Slide 3
Company profile Shenzhen Hongmei Power Semiconductor is a leading power semiconductor device design and sales enterprise in china, specializing in the design, production and sales of power semiconductor devices，we offer one station / cost effctive solution supplier of power semiconductor device.
Since its establishment, Hongmei Power Semiconductor has developed rapidly，its products have covered MOS(Low voltage MOS/medium voltage and high current MOS/SGT MOS/High voltage SJ MOS/High voltage panar MOS)、IGBT、SiC diode、GaN PowerFET etc... about more than 900 model products .
The follow key promoted and specialty products are introduced to you .

## Slide 4: 2.储能/BMS/电动车/平衡车 SGT MOS
Energy storage products SGT MOS
1.Sic二极管/GaN FET/IGBT单管
Energy storage products SGT MOS |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max) (BVDSS(V) | ID(Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON)@ 10VTyp(mΩ)
HMS260N10/D/LL | SGT (Split Gate) | TO-220/TO-263/ TOLL-8L | Nch | 100V | 260A | 780A | 3.0V | ±20 | 2.3mΩ
HMS310N85/D/LL | SGT (Split Gate) | TO-220/TO-263/ TOLL-8L | Nch | 85V | 310A | 960A | 3.0V | ±20 | 1.6mΩ
HMS330N06/D/LL | SGT (Split Gate) | TO-220/TO-263/ TOLL-8L | Nch | 60V | 330A | 990A | 3.0V | ±20 | 1.4mΩ
HMS320N04/D/G/LL | SGT (Split Gate) | TO-220/TO-263/ PDFN5X6-8L/TOLL-8L | Nch | 40V | 320A | 960A | 1.9V | ±20 | 0.5mΩ
Advantage：The newest SGT technology，package : TOLL-8L/TO-263/TO-220/PDFN5X6-8L , can used in different products； have a testing of VTH，can used in paralleling structure application。
Application：Energy storage products、Outdoor power supply products。

## Slide 5: 2-2
BMS/E-bicycle/Balance vehicle SGT MOS
1.Sic二极管/GaN FET/IGBT单管
BMS/E-bicycle/Balance vehicle SGT MOS |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max) (BVDSS(V) | ID(Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON)@ 10VTyp(mΩ)
HMS135N10/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 100V | 135A | 405A | 3.0V | ±20 | 3.4mΩ
HMS120N10/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 100V | 120A | 360A | 3.0V | ±20 | 4.6mΩ
HMS85N10/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 100V | 85A | 255A | 3.0V | ±20 | 7.0mΩ
HMS80N10/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 100V | 80A | 240A | 3.0V | ±20 | 7.5mΩ
HMS135N85/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 85V | 135A | 405A | 3.0V | ±20 | 3.3mΩ
HMS120N85/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 85V | 120A | 360A | 3.0V | ±20 | 4.5mΩ
HMS100N85/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 85V | 100A | 300A | 3.0V | ±20 | 5.4mΩ
HMS80N85/D/G/K | SGT (Split Gate) | TO-220/TO-263 PDFN5X6-8L/TO-252 | Nch | 85V | 80A | 240A | 3.0V | ±20 | 6.9mΩ
HMS100N15/D | SGT (Split Gate) | TO-220/TO-263 | Nch | 150V | 100A | 300A | 3.0V | ±20 | 6.5mΩ
HMS100N20/D | SGT (Split Gate) | TO-220/TO-263 | Nch | 200V | 100A | 300A | 3.0V | ±20 | 9.3mΩ
HMS80N25/D | SGT (Split Gate) | TO-220/TO-263 | Nch | 250V | 80A | 240A | 3.0V | ±20 | 18mΩ
Advantage：
The newest SGT technology，package :TO-263/TO-220/PDFN5X6-8L /
TO-252 , can used in different products； have a testing of VTH，can used in paralleling structure application。
Application：
BMS/E-bicycle/
Balance vehicle/ Scooter/Portable energy storage
/Outdoor power supply

## Slide 6
Super-junction high voltage MOS
1.Sic二极管/GaN FET/IGBT单管
Super-junction high voltage MOS |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON)@10V Typ(mΩ) | Feature
HMS5N65R /R2 | Super-Junction | SOT223-3L/ SOT223-2L | Nch/ ESD | 650V | 5A | 15A | 3V | 20V | 950mΩ | Multi-layer technology
HMS11N65Q | Super-Junction | DFN5X6-8L | Nch/ ESD | 650V | 11A | 33A | 3V | 30V | 300mΩ | 
HMS13N65Q | Super-Junction | DFN5X6-8L | Nch | 650V | 13A | 39A | 3V | 30V | 240mΩ | 
HMS15N65Q | Super-Junction | DFN5X6-8L | Nch | 650V | 15A | 45A | 3V | 30V | 230mΩ | 
HMS5N70R /R2 | Super-Junction | SOT223-3L/ SOT223-2L | Nch/ ESD | 700V | 5A | 15A | 3V | 30V | 955mΩ | Multi-layer technology
HMS11N70Q | Super-Junction | DFN5X6-8L | Nch/ ESD | 700V | 11A | 30A | 3V | 30V | 400mΩ | 
HMS15N70Q | Super-Junction | DFN5X6-8L | Nch | 700V | 15A | 45A | 3V | 30V | 300mΩ | 
HMS5N90R /R2 | Super-Junction | SOT223-3L/ SOT223-2L | Nch | 900V | 5A | 15A | 3.5V | 30V | 1480mΩ | Multi-layer technology
Advantage：
SOT-223/ DFN5X6 package，idea for small prodects。
Multi-layer-tech，ESD protection，strongger impact capacity
Application：
GaN fast charger/charger/Adapter/smart socket/Appliance Power supply /LED driver/LED lighting

## Slide 7: 3-2
800V Super-junction high voltage MOS
1.Sic二极管/GaN FET/IGBT单管
800V Super-junction high voltage MOS |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON)@ 10VTyp(mΩ) | Feature
HMS5N80/ F/K/I/R/R2 | Super-Junction | TO-220/TO-220F/ TO-252/TO-251/ SOT223-3L/SOT223-2L | Nch/ ESD | 800V | 5A | 15A | 3.5V | 30V | 1050mΩ | Multi-layer technology
HMS7N80/ F/K/I | Super-Junction | TO-220/TO-220F/ TO-252/TO-251 | Nch/ ESD | 800V | 7A | 21A | 3V | 30V | 740mΩ | Multi-layer technology
HMS10N80/F/K | Super-Junction | TO-220/TO-220F/ TO-252 | Nch/ ESD | 800V | 10A | 30A | 30V | 30V | 580mΩ | Multi-layer technology
HMS15N80/F/D | Super-Junction | TO-220/TO-220F/ TO-263 | Nch/ ESD | 800V | 15A | 45A | 30V | 30V | 330mΩ | Multi-layer technology
HMS20N80/F/D/T | Super-Junction | TO-220/TO-220F/ TO-263/TO-247 | Nch/ ESD | 800V | 20A | 60A | 3V | 20V | 220mΩ | Multi-layer technology
Advantage：Multi-layer-tech，ESD protection，strongger impact capacity
Application：Super-charger station/OBC.

## Slide 8: 4.高压平面MOS特色产品
Small SMD package planar high voltage MOS
1.Sic二极管/GaN FET/IGBT单管
Small SMD package Planar high voltage MOS |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON)@10V Typ(mΩ)
HM0565MR | planar | SOT23-3L | Nch | 650V | 0.5A | 2A | 3V | 30V | 9Ω
HM1N60R/PR | planar | SOT-223/SOT-89 | Nch | 600V | 1.3A | 5A | 3V | 30V | 11Ω
HM4N60R | planar | SOT-223 | Nch | 600V | 4A | 16A | 3V | 30V | 1.7Ω
HM2N65R/PR | planar | SOT-89 | Nch | 650V | 2A | 6A | 3V | 30V | 7.8Ω
HM4N65R | planar | SOT-223 | Nch | 650V | 4A | 16A | 3V | 30V | 2.4Ω
HM1N50MR | planar | SOT23-3L | Nch | 500V | 1A | 3A | 3V | 30V | 9.2Ω
HM2N50R/PR | planar | SOT-223/SOT-89 | Nch | 500V | 2A | 4A | 3V | 30V | 5.0Ω
HM5N50R | planar | SOT-223 | Nch | 500V | 5A | 20A | 3V | 30V | 1.5Ω
HM1N70R/PR | planar | SOT-223/SOT-89 | Nch | 700V | 1A | 4A | 3V | 30V | 10.5Ω
HM2N70R | planar | SOT-223 | Nch | 700V | 2A | 8A | 3V | 30V | 4.7Ω
HM3N40R/PR | planar | SOT-223/SOT-89 | Nch | 400V | 3A | 9A | 3V | 30V | 2.8Ω
HM3N30R/PR | planar | SOT-223/SOT-89 | Nch | 300V | 3A | 12A | 2.7V | 25V | 2.6Ω
HM5N30R/PR | planar | SOT-223/SOT-89 | Nch | 300V | 5A | 15A | 2.7V | 25V | 1.2Ω
HM2N25MR | Trench | SOT23-3L | Nch | 250V | 2A | 10A | 2.5V | 20V | 1.3Ω
HM3N25R | planar | SOT-223 | Nch | 250V | 3A | 12A | 3V | 20V | 1Ω
HM3N20M/PR | planar | SOT23-3L/SOT-89 | Nch | 200V | 3A | 9A | 3V | 20V | 1Ω
Advantage：
SOT23-3L/ SOT-89/SOT-223 package，can used in small size products。
Application：
Charger/Adapter/Smart socket/
Appliance power supply/LED driver /LED lighting/
Leakage protection switch

## Slide 9: 4.高压平面MOS特色产品
TO-263 SMD Package Planar high voltage high current MOS
1.Sic二极管/GaN FET/IGBT单管
TO-263 SMD package Planar high voltage and high current MOS |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON)@10V Typ(mΩ)
HM10N65D | planar | TO-263 | Nch | 650V | 10A | 40A | 3V | 30V | 0.7Ω
HM12N65D | planar | TO-263 | Nch | 650V | 12A | 48A | 3V | 30V | 0.63Ω
HM13N50D | planar | TO-263 | Nch | 500V | 13A | 52A | 3V | 30V | 0.4Ω
HM25N50D | planar | TO-263 | Nch | 500V | 25A | 100A | 3V | 20V | 0.21Ω
Advantage：Planar high voltage and high current MOS，TO-263 SMD package，can used in thin-lightweight products。
Application：Charger / Adapter / Smart socket / Appliance power supply / LED driver/LED lighting

## Slide 10: 5.超高压平面MOS及高压PMOS
Planar Ultra-high voltage MOS
1.Sic二极管/GaN FET/IGBT单管
Planar Ultra-high voltage MOS |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max)(BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @10V Typ(mΩ)
HM01N100PR | planar | SOT-89 | Nch | 1000V | 0.1A | 0.3A | 3V | 30V | 46Ω
HM3N100/F/D | planar | TO-220/TO-220F/ TO-263 | Nch | 1000V | 3A | 12A | 3.5V | 30V | 3.5Ω
HM8N100F/A | planar | TO-220F/TO-3P | Nch | 1000V | 8A | 24A | 3.5V | 30V | 1.18Ω
HM3N120/F/A | planar | TO-220/TO-220F/ TO-3P | Nch | 1200V | 3A | 12A | 4V | 30V | 5.1Ω
HM3N150/F/A | planar | TO-220/TO-220F/ TO-3P | Nch | 1500V | 3A | 12A | 4V | 30V | 5Ω
Application：Charger station / PV inverter / Servo-driver / Power supply / Welding machine / UPS / Frequency converter。

## Slide 11: 5-2
High voltage P channel MOSFET
1.Sic二极管/GaN FET/IGBT单管
Trench high voltage P channel MOSFET |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max) (BVDSS(V) | ID(Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ)
HM1P15MR | Trench | SOT23-3L | Pch | -150V | -1A | -4A | -3.0V | -20V | 780mΩ | 980mΩ
HM4489 | Trench | SOP8 | Pch | -150V | -2A | -8A | -3.0V | -20V | 780mΩ | 980mΩ
HM2P15R/PR | Trench | SOT-223/SOT-89 | Pch | -150V | -2A | -8A | -3.0V | -20V | 780mΩ | 980mΩ
HM4P15Q | Trench | DFN3X3-8L | Pch | -150V | -4A | -12A | -3.0V | -20V | 780mΩ | 980mΩ
HM5P15D | Trench | DFN5X6-8L | Pch | -150V | -5A | -15A | -3.0V | -20V | 780mΩ | 980mΩ
HM6P15K | Trench | TO-252 | Pch | -150V | -6A | -18A | -3.0V | -20V | 780mΩ | 980mΩ
HM25P15K | Trench | TO-252 | Pch | -150V | -25A | -100A | -1.9V | -20V | 120mΩ | 131mΩ
HM4P20K | Trench | TO-252 | Pch | -200V | -4A | -12A | -3.0V | -20V | 1250mΩ | 
HM2P20Q/D | Trench | PDFN3X3-8L/ DFN5X6-8L | Pch | -200V | -2A | -6A | -3.0V | -20V | 1250mΩ | 
HM1P20 | Trench | SOP-8 | Pch | -200V | -1A | -3A | -3.0V | -20V | 1250mΩ | 
HM11P20/D | Trench | TO-220/TO-263 | Pch | -200V | -11A | -33A | -3.0V | -20V | 240mΩ | 
HM02P30R/PR | Trench | SOT-223/SOT-89 | Pch | -300V | -0.2A | -0.6A | -0.85V | -20V | 17mΩ | 30mΩ
HM05P35MR | Trench | SOT23-3L | Pch | -350V | -0.5A | -1.5A | -1.4V | +/-20V | 15.5mΩ | 
HM4889 | Trench | SOP8 | 2 Pch | -150V | -2A | -8A | -3.0V | -20V | 780mΩ | 980mΩ
Advantage：Maximum Vds is above 150V，have a highest voltage 350V；have SOT23-3L/SOT-89/SOT-223/SOP8/DFN3X3-8L/ DFN5X6-8L/TO-252 package to used in different application。

## Slide 12: 6.全桥/半桥驱动MOS
Full-bridge structure MOSFET
1.Sic二极管/GaN FET/IGBT单管
Trench Full-bridge structure MOSFET |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max) (N/P)(BVDSS(V) | ID(Max) (N/P)(ID(A))
HM4922 | Trench | SOP8 | 2 Nch + 2 Pch | 20V/-20V | 12A/-7A
HM4923 | Trench | SOP8 | 2 Nch + 2 Pch | 30V/-30V | 12A/-8A
HM4924 | Trench | SOP8 | 2 Nch + 2 Pch | 40V/-40V | 10A/-6A
HM4926 | Trench | SOP8 | 2 Nch + 2 Pch | 60V/-60V | 5A/-5A
HM4920 | Trench | SOP8 | 2 Nch + 2 Pch | 100V/-100V | 4A/-3A
Advantage：A Full-bridge structure circuit which 2 Nch MOS and 2 Pch MOS is packaged in a SOP-8 device ，it can save PCB size.
Application：Wire-less charger / USB PD fast-charger / Full-bridge structure circuit / Fascial gun / High speed air blower / Smart door-lock / Drone / Model airplane / Moto driver

## Slide 13: 6-2
Half-bridge structure MOSFET
Trench half-bridge structure MOSFET |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max) (BVDSS(V) | ID(Max) (ID(A))
HM40SDN02Q | Trench | DFN3X3-8L | 2 Nch / series half-bridge | 20V | 40A/40A
HM25SDN03Q | Trench | DFN3X3-8L | 2 Nch / series half-bridge | 30V | 25A/25A
HM20SDN04Q | Trench | DFN3X3-8L | 2 Nch / series half-bridge | 40V | 20A/20A
HM10SDN06Q | Trench | DFN3X3-8L | 2 Nch / series half-bridge | 60V | 10A/10A
HM08SDN10Q | Trench | DFN3X3-8L | 2 Nch / series half-bridge | 100V | 8A/8A
HM30SDN02D | Trench | DFN5X6-8L | 2 Nch / series half-bridge | 20V | 30A/30A
HM35SDN03D | Trench | DFN5X6-8L | 2 Nch / series half-bridge | 30V | 35A/35A
HM18SDN04D | Trench | DFN5X6-8L | 2 Nch / series half-bridge | 40V | 18A/18A
HM10SDN06D | Trench | DFN5X6-8L | 2 Nch / series half-bridge | 60V | 10A/10A
HM10SDN10D | Trench | DFN5X6-8L | 2 Nch / series half-bridge | 100V | 10A/10A
Advantage：
A Half-bridge structure circuit which 2 Nch MOS is packaged in a DFN3X3-8L/DFN5X6-8L device，used in small size products application 。
Application：
Wire-less charger / USB PD fast-charger / Full-bridge structure circuit / Fascial gun / High speed air blower / Smart door-lock / Drone / Model airplane / Moto driver

## Slide 14: 7.双N/双P/N+P 中压大电流MOS
2 Nch medium voltage and high current MOSFET
1.Sic二极管/GaN FET/IGBT单管
Application：
Wire-less charger / USB PD fast-charger / Full-bridge structure circuit / Fascial gun / High speed air blower / Smart door-lock / Drone / Model airplane / Moto driver
2 Nch medium voltage and high current MOSFET |  |  |  |  | 
Part Number | Technology | Package | Polarity / structure | VDS(Max) (BVDSS(V) | ID(Max) (ID(A))
HM30DN02D | Trench | DFN5X6-8L | 2 Nch / L/R | 20V | 30A/30A
HM4884Q | Trench | DFN3X3-8L | 2 Nch / L/R | 30V | 28A/28A
HM35DN03D | Trench | DFN5X6-8L | 2 Nch / L/R | 30V | 35A/35A
HM20DN04Q/D | Trench | DFN3X3-8L/ DFN5X6-8L | 2 Nch / L/R | 40V | 20A/20A
HM40DN04K | Trench | TO-252-4L | 2 Nch / L/R | 40V | 40A/40A
HM10DN06Q/D | Trench | DFN3X3-8L/ DFN5X6-8L | 2 Nch / L/R | 60V | 10A/10A
HM20DN06KA | Trench | TO-252-4L | 2 Nch / L/R | 60V | 20A/20A
HM08DN10D | Trench | DFN5X6-8L | 2 Nch / L/R | 100V | 8A/8A
HMS10DN10Q | SGT (Trench) | DFN3X3-8L | 2 Nch / L/R | 100V | 10A/10A
HMS10DN08Q | SGT (Trench) | DFN3X3-8L | 2 Nch / L/R | 80V | 10A/10A
HMS30DN08D | SGT (Trench) | DFN5X6-8L | 2 Nch / L/R | 80V | 30A/30A

## Slide 15: 7-2
2 Pch medium voltage and high current MOSFET
1.Sic二极管/GaN FET/IGBT单管
2 Pch medium voltage and high current MOSFET |  |  |  |  | 
Part Number | Technology | Package | Polarity / structure | VDS(Max) (BVDSS(V) | ID(Max) (ID(A))
HM18DP02Q | Trench | DFN3X3-8L | 2 Pch / L/R | -20V | -18A/-18A
HM18DP03Q/D | Trench | DFN3X3-8L/DFN5X6-8L | 2 Pch / L/R | -30V | -18A/-18A
HM12DP04Q | Trench | DFN5X6-8L | 2 Pch / L/R | -40V | -12A/-12A
HM10DP06D | Trench | DFN5X6-8L | 2 Pch / L/R | -60V | -10A/-10A
HM06DP10Q | Trench | DFN3X3-8L | 2 Pch / L/R | -100V | -6A/-6A
HM07DP10D | Trench | DFN5X6-8L | 2 Pch / L/R | -100V | -7A/-7A
Application：
Wire-less charger / USB PD fast-charger / Full-bridge structure circuit / Fascial gun / High speed air blower / Smart door-lock / Drone / Model airplane / Moto driver

## Slide 16: 7-2
Nch+Pch medium voltage and high current MOSFET
1.Sic二极管/GaN FET/IGBT单管
Nch + Pch medium voltage and high current MOSFET |  |  |  |  | 
Part Number | Technology | Package | Polarity / structure | VDS(Max) (BVDSS(V) | ID(Max) (ID(A))
HM605K | Trench | TO-252-4L | Nch + Pch / L/R | 20V/-20V | 45A/-35A
HM607K | Trench | TO-252-4L | Nch + Pch / L/R | 30V/-30V | 35A/-25A
HM609K | Trench | TO-252-4L | Nch + Pch / L/R | 40V/-40V | 30A/-18A
HM603K | Trench | TO-252-4L | Nch + Pch / L/R | 60V/-60V | 20A/-15A
HM610K | Trench | TO-252-4L | Nch + Pch / L/R | 100V/-100V | 15A/-13A
HM4616Q | Trench | DFN3X3-8L | Nch + Pch / L/R | 30V/-30V | 28A/-18A
HM4618Q | Trench | DFN3X3-8L | Nch + Pch / L/R | 40V/-40V | 20A/-12A
HM4611Q | Trench | DFN3X3-8L | Nch + Pch / L/R | 60V/-60V | 10A/-10A
HM4615Q | Trench | DFN3X3-8L | Nch + Pch / L/R | 100V/-100V | 8A/-6A
HM4622D | Trench | DFN5X6-8L | Nch + Pch / L/R | 20V/-20V | 30A/-35A
HM4616D | Trench | DFN5X6-8L | Nch + Pch / L/R | 30V/-30V | 35A/-18A
HM4618D | Trench | DFN5X6-8L | Nch + Pch / L/R | 40V/-40V | 20A//-12A
HM4611D | Trench | DFN5X6-8L | Nch + Pch / L/R | 60V/-60V | 10A/-10A
HM4615D | Trench | DFN5X6-8L | Nch + Pch / L/R | 100V/-100V | 10A/-7A
Application：Wire-less charger / USB PD fast-charger / Full-bridge structure circuit / Fascial gun / High speed air blower / Smart door-lock / Drone / Model airplane / Moto driver

## Slide 17: 8.超轻薄低压MOS
Ultra-weight Ultra-thin package low voltage MOSFET
1.Sic二极管/GaN FET/IGBT单管
DFN1006-3L package low voltage MOSFET |  |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ) | RDS(ON) @-2.5V Typ(mΩ)
HM2301DR | Trench | DFN1006-3L | Pch / ESD protection | -20V | -0.8A | -4A | -0.45V | -6V |  | 350mΩ | 440mΩ
HM2302DR | Trench | DFN1006-3L | Pch / ESD protection | 20V | 0.9A | 3.6A | 0.45V | 6V |  | 220mΩ | 260mΩ
Advantage：Ultra-low Vth；have a ESD protection diode between Gate and Source
Application：TWS Bluetooth earphone / Smart watch / Smart ring / Other smart wearable products / E-cigarettes

## Slide 18: 8-2.1
Ultra-weight Ultra-thin package low voltage MOSFET
1.Sic二极管/GaN FET/IGBT单管
DFN2X2-6L package low voltage MOSFET |  |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ) | RDS(ON) @-2.5V Typ(mΩ)
HM09P12D | Trench | DFN2X2-6L | Pch | -12V | -9A | -27A | -0.6V | -12V |  | 17mΩ | 24mΩ
HM16P12D | Trench | DFN2X2-6L | Pch | -12V | -16A | -65A | -0.7V | -12V |  | 11.5mΩ | 14mΩ
HM2305D | Trench | DFN2X2-6L | Pch | -20V | -8A | -32A | -0.7V | -12V |  | 39mΩ | 58mΩ
HM3401DR | Trench | DFN2X2-6L | Pch | -30V | -6A | -30A | -1.0V | -12V | 50mΩ | 64mΩ | 95mΩ
HM2319D | Trench | DFN2X2-6L | Pch | -40V | -7A | -21A | -1.5V | -20V | 73mΩ | 98mΩ | 
HM2309DR | Trench | DFN2X2-6L | Pch | -60V | -4A | -16A | -1.8V | -20V | 188mΩ | 266mΩ | 
HM4P10D | Trench | DFN2X2-6L | Pch | -100V | -4A | -12A | -1.4V | -20V | 210mΩ | 225mΩ | 
HM2803D | Trench | DFN2X2-6L | 2 Pch | -20V | -5A | -15A | -0.7V | -12V |  | 39mΩ | 58mΩ
HM3801DR | Trench | DFN2X2-6L | 2 Pch | -30V | -6A | -30A | -1.0V | -12V | 50mΩ | 60mΩ | 95mΩ
HM2819D | Trench | DFN2X2-6L | 2 Pch | -40V | -5A | -15A | -1.5V | -20V |  | 73mΩ | 110mΩ
HM2809D | Trench | DFN2X2-6L | 2 Pch | -60V | -3A | -12A | -1.8V | -20V | 188mΩ | 266mΩ | 
Application：TWS Bluetooth earphone / Smart watch / Smart ring / Other smart wearable products / E-cigarettes

## Slide 19: 8-2.2
Ultra-weight Ultra-thin package low voltage MOSFET
1.Sic二极管/GaN FET/IGBT单管
DFN2X2-6L package low voltage MOSFET |  |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS(Max) (BVDSS(V) | ID(Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ) | RDS(ON) @-2.5V Typ(mΩ)
HM2300DR | Trench | DFN2X2-6L | Nch | 20V | 8A | 32A | 0.65V | 12V |  | 22mΩ | 33mΩ
HM3400DR | Trench | DFN2X2-6L | Nch | 30V | 8A | 32A | 0.9V | 12V | 31mΩ | 34mΩ | 45mΩ
HM2318D | Trench | DFN2X2-6 | Nch | 40V | 6A | 20A | 1.0V | 20V | 32mΩ | 50mΩ | 
HM2310DR | Trench | DFN2X2-6L | Nch | 60V | 4A | 12A | 1.1V | 20V | 105mΩ | 125mΩ | 
HM4N10D | Trench | DFN2X2-6L | Nch | 100V | 4A | 16A | 1.5V | 20V | 135mΩ |  | 
HM2800D | Trench | DFN2X2-6L | 2 Nch | 20V | 5A | 15A | 0.65V | 12V |  | 22mΩ | 33mΩ
HM3800D | Trench | DFN2X2-6L | 2 Nch | 30V | 5.8A | 24A | 0.9V | 12V | 31mΩ | 34mΩ | 45mΩ
HM2818D | Trench | DFN2X2-6L | 2 Nch | 40V | 4.0A | 12A | 1.0V | 20V |  | 33mΩ | 46mΩ
HM2810D | Trench | DFN2X2-6L | 2 Nch | 60V | 3.0A | 12A | 1.1V | 20V | 78mΩ | 84mΩ | 
HM3DN10D | Trench | DFN2X2-6L | 2 Nch | 100V | 3.0A | 9.0A | 1.8V | 20V | 210mΩ |  | 
HM4620D | Trench | DFN2X2-6L | Nch+Pch | 20V/-20V | 5A/-5A | 15A/-15A | 0.65/-0.7V | 12V/-12V |  | 29mΩ/78mΩ | 35mΩ/102mΩ
HM4630D | Trench | DFN2X2-6L | Nch+Pch | 30V/-30V | 5A/-5A | 15A/-15A | 0.9/-0.9V | 12V/-12V |  | 30mΩ/60mΩ | 46mΩ/95mΩ
HM4640D | Trench | DFN2X2-6L | Nch+Pch | 40V/-40V | 4A/-5A | 16A/-20A | 3.0/-1.8V | 20V/-20V |  | 33mΩ/72mΩ | 46mΩ/110mΩ
Application：TWS Bluetooth earphone / Smart watch / Smart ring / Other smart wearable products / E-cigarettes

## Slide 20: 8-3
Ultra-weight Ultra-thin package low voltage MOSFET
1.Sic二极管/GaN FET/IGBT单管
SOT-323 package low voltage MOSFET |  |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ) | RDS(ON) @-2.5V Typ(mΩ)
HM2301KR | Trench | SOT-323 | Pch | -20V | -3.0A | -6A | -0.65V | -12V |  | 64mΩ | 89mΩ
HM2301BKR | Trench | SOT-323 | Pch / ESD protection | -20V | -0.8A | -1.6A | -0.45V | -6V |  | 350mΩ | 440mΩ
BSS84KR | Trench | SOT-323 | Pch | -55V | -0.3A | -0.9A | -1.5V | -20V | 2.5Ω | 3.0Ω | 
HM2302KR | Trench | SOT-323 | Nch | 20V | 3A | 6A | 0.7V | 10V |  | 30mΩ | 37mΩ
HM2302BKR | Trench | SOT-323 | Nch / ESD protection | 20V | 0.9A | 1.8A | 0.45V | 8V |  | 220mΩ | 260mΩ
HM3400KR | Trench | SOT-323 | Nch | 30V | 0.8A | 3.2A | 1.0V | 10V |  | 280mΩ | 370mΩ
BSS138KR | Trench | SOT-323 | Nch | 50V | 0.34A | 1.36A | 1.2V | 20V |  | 1.0Ω | 1.2Ω
HM7002KR | Trench | SOT-323 | Nch / ESD protection | 60V | 0.3A | 1.2A | 1.6V | 20V | 1.4Ω | 1.8Ω | 
Application：TWS Bluetooth earphone / Smart watch / Smart ring / Other smart wearable products / E-cigarettes

## Slide 21: 8-4
Ultra-weight Ultra-thin package low voltage MOSFET
1.Sic二极管/GaN FET/IGBT单管
SOT-523 package low voltage MOSFET |  |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ) | RDS(ON) @-2.5V Typ(mΩ)
HM2301BSR | Trench | SOT-523 | Pch / ESD protection | -20V | -0.8A | -1.6A | -0.45V | -6V |  | 350mΩ | 440mΩ
BSS84SR | Trench | SOT-523 | Pch | -55V | -0.3A | -0.9A | -1.5V | -20V | 2.5Ω | 3.0Ω | 
HM2302BSR | Trench | SOT-523 | Nch / ESD protection | 20V | 0.9A | 1.8A | 0.45V | 8V |  | 220mΩ | 260mΩ
BSS138SR | Trench | SOT-523 | Nch | 50V | 0.34A | 1.36A | 1.2V | 20V |  | 1.0Ω | 1.2Ω
Application：TWS Bluetooth earphone / Smart watch / Smart ring / Other smart wearable products / E-cigarettes

## Slide 22: 8-5
Ultra-weight Ultra-thin package low voltage MOSFET
1.Sic二极管/GaN FET/IGBT单管
SOT-723 package low voltage MOSFET |  |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ) | RDS(ON) @-2.5V Typ(mΩ)
HM2301BJR | Trench | SOT-723 | Pch / ESD protection | -20V | -0.8A | -1.6A | -0.45V | -6V |  | 350mΩ | 440mΩ
HM2302BJR | Trench | SOT-723 | Nch / ESD protection | 20V | 0.9A | 1.8A | 0.45V | 8V |  | 220mΩ | 260mΩ
Advantage：Ultra-low Vth；have a ESD protection diode between Gate and Source
Application：TWS Bluetooth earphone / Smart watch / Smart ring / Other smart wearable products / E-cigarettes

## Slide 23: 8-6
Ultra-weight Ultra-thin package low voltage MOSFET
1.Sic二极管/GaN FET/IGBT单管
SOT-363 package low voltage MOSFET |  |  |  |  |  |  |  |  |  |  | 
Part Number | Technology | Package | Polarity | VDS (Max) (BVDSS(V) | ID (Max) (ID(A)) | IDM | VTH (Typ) | VGS | RDS(ON) @-10V Typ(mΩ) | RDS(ON) @-4.5V Typ(mΩ) | RDS(ON) @-2.5V Typ(mΩ)
HM2301BWKR | Trench | SOT-363 | 2 Pch / ESD protection | -20V | -0.8A | -4A | -0.45V | -8V | 350mΩ | 550mΩ | 780mΩ
BSS84DW | Trench | SOT-363 | 2 Pch | -55V | -0.3A | -0.9A | -1.5V | -20V | 3.0Ω | 2.5Ω | 
HM2302BWKR | Trench | SOT-363 | 2 Nch / ESD protection | 20V | 0.9A | 3.6A | 0.45V | 8V |  | 220mΩ | 260mΩ
BSS138DW | Trench | SOT-363 | 2 Nch | 50V | 0.34A | 1.36A | 1.2V | 20V |  | 1.0Ω | 1.2Ω
HM7002KDW | Trench | SOT-363 | 2 Nch / ESD protection | 60V | 0.32A | 1.5A | 1.7V | 20V | 2.3Ω | 2.7Ω | 
HM6604BWKR | Trench | SOT-363 | Nch+Pch/ ESD protection | 20V/20V | 0.9A/-0.8A | 5.0A/-4.0A | 0.45V/-0.45V | 8V/-8V | 220mΩ/ 350mΩ | 260mΩ/ 550mΩ | 330mΩ/ 780mΩ
Application：TWS Bluetooth earphone / Smart watch / Smart ring / Other smart wearable products / E-cigarettes

## Slide 24: 1.Sic二极管/GaN FET/IGBT单管
Advantage：Auto-grade wafer,it is manufactured in standard of TS16949，support 8 times surge current ；package is met standard of Auto-grade，the device can pass AEC-Q101。
Application：New energy vehicle / OBC / Super-charge station 。
充电：
Auto-grade Sic diode
Auto-grade SiC diode |  |  |  |  |  |  |  |  |  |  | 
Part Number | Vrrm | Ir |  | If |  |  | Ifsm | QC | Tj | Feature | Package
 |  | Tj=25℃ | Tj=175℃ | Tc=25℃ | Tc=135℃ | Tc=150℃ |  |  |  |  | 
HMC15N65/D/T2 | 650V | 3uA | 20uA | 43A | 19.5A | 15A | 120A | 47nC | -55℃--175℃ | Faster switching speed whether temperature，high operating frequency，fast reverse recovery time，suppressing high surge currents | TO-220-2L/ TO-263/ TO-247-2L
HMC20N65/D/T2 | 650V | 5uA | 30uA | 50.1A | 23.4A | 20A | 100A | 47.9nC | -55℃--175℃ | Faster switching speed whether temperature，high operating frequency，fast reverse recovery time，suppressing high surge currents | TO-220-2L/ TO-263/ TO-247-2L
HMC5N120/K | 1200V | 2uA | 11uA | 20A | 9.7A | 5A | 51A | 36nC | -55℃--175℃ | Faster switching speed whether temperature，high operating frequency，fast reverse recovery time，suppressing high surge currents | TO-220-2L/ TO-252
HMC8N120/K | 1200V | 3uA | 20uA | 28A | 13A | 8A | 68A | 53nC | -55℃--175℃ | Faster switching speed whether temperature，high operating frequency，fast reverse recovery time，suppressing high surge currents | TO-220-2L/ TO-252
HMC20N120/D/T2 | 1200V | 8uA | 50uA | 49.1A | 23.5A | 20A | 125A | 94nC | -55℃--175℃ | Faster switching speed whether temperature，high operating frequency，fast reverse recovery time，suppressing high surge currents | TO-220-2L/ TO-263/ TO-247-2L

## Slide 25: 1.Sic二极管/GaN FET/IGBT单管
Application：
DC-DC power module / LED driver / OBC / UPS / charge station / Service power supply/PV inverter/Communication power supply；
PDFN5X6 package can used in GaN fast-charger 。
充电：
Sic diode
SiC diode |  |  |  |  |  |  |  |  | 
Part Number | Vr | Vf | If | Ifsm | Qc | Tj | Rθjc | Rθja | Package
HMC2N65/K | 650V | 1.4V | 2A | 20A | 5.4nC | -55-175 ℃ | 3.8 ℃/W | 80 ℃/W | TO-220-2L/ TO-252-2L
HMC4N65/K | 650V | 1.4V | 4A | 40A | 9nC | -55-175 ℃ | 2.9 ℃/W | 80 ℃/W | TO-220-2L/ TO-252-2L
HMC6N65/K/Q | 650V | 1.4V | 6A | 60A | 13nC | -55-175 ℃ | 2.9 ℃/W | 80 ℃/W | TO-220-2L/ TO-252-2L/ PDFN5X6
HMC8N65/K/Q | 650V | 1.4V | 8A | 80A | 18nC | -55-175 ℃ | 2.9 ℃/W | 80 ℃/W | TO-220-2L/ TO-252-2L/ PDFN5X6
HMC10N65/K/Q | 650V | 1.4V | 10A | 86A | 23nC | -55-175 ℃ | 3.0 ℃/W | 80 ℃/W | TO-220-2L/ TO-252-2L/ PDFN5X6
HMC2N120/K | 1200V | 1.55V | 2A | 20A | 8nC | -55-175 ℃ | 2.55 ℃/W | 80 ℃/W | TO-220-2L/ TO-252-2L

## Slide 26: 1-2
GaN PowerFET
GaN PowerFET |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Part Number | Polarity | structure | VDS (Max) | VTH | ID (Max) | RDS(on) (Max) | Qg | Qrr | Ciss | Coss | Crss | Tj | Rθjc | Rθja | Package
HMN9N65D/Q | Nch | D-mode integrated a Si MOS | 650V | 1.65V | 9A | 220 mohm | 18nC | 50nC | 1150pF | 25pF | 1pF | -55-150℃ | 4.5℃/W | 50℃/W | DFN8X8-2L DFN5X6-2L
HMN11N65D | Nch | D-mode integrated a Si MOS | 650V | 1.65V | 11A | 125 mohm | 20nC | 56nC | 1050pF | 56pF | 2pF | -55-150℃ | 1.8℃/W | 50℃/W | DFN8X8-2L
Advantage：D-mode structure，package with Si Depletion Mode MOSFET，simple application circuit，can directly replace America Transphorm-Brand products，faster switch speed，ultra low Qg，wider Gate safety margin，strongger noise immunity。
Application：GaN fast charger / QR fast charger / LLC power supply / charger / adapter / solor inverter / switch power supply

## Slide 27: 1-3
IGBT
IGBT |  |  |  |  |  |  |  |  |  | 
Part Number | Polarity | Vces (Max) | Vges | Vge (th) | Ic(Typ/ 100℃) | Ic(Max/ 25℃) | Icm MAX | Pd MAX | Package | Application
HMG20N65/F/D | N-IGBT / TrenchSop | 650V | 30V | 5V | 20A | 40A | 80A | 105W | TO-220/TO-220F/ TO-263 | Frequency converter/ Appliance/Moto driver medi-high-freq products
HMG40N65AT | N-IGBT / TrenchSop | 650V | 20V | 5V | 40A | 80A | 120A | 155W | TO-247 | Frequency converter/ Appliance/Moto driver medi-high-freq products
HMG40N65FT | N-IGBT / High-speed switch TrenchSop | 650V | 20V | 5V | 40A | 80A | 120A | 155W | TO-247 | IH heater/Inductor cooker/ Rice cooker/ Inverter / Welding/UPS / PFC high-freq products
HMG75N65AT | N-IGBT / TrenchSop | 650V | 30V | 5V | 75A | 150A | 300A | 468W | TO-247 | Frequency converter/ Appliance/Moto driver medi-high-freq products
HM25N120FT | N-IGBT / High-speed switch TrenchSop | 1200V | 20V | 6V | 25A | 50A | 50A | 536W | TO-247 | IH heater/Inductor cooker/ Rice cooker/ Inverter / Welding/UPS / PFC high-freq products
HM40N120AT | N-IGBT / TrenchSop | 1200V | 30V | 5V | 40A | 80A | 160A | 416W | TO-247 | Frequency converter/ Appliance/Moto driver medi-high-freq products
HM40N120FT | N-IGBT / High-speed switch TrenchSop | 1200V | 30V | 5V | 40A | 80A | 160A | 417W | TO-247 | IH heater/Inductor cooker / Rice cooker/ Inverter / Welding/UPS / PFC high-freq products
Application：
1. Industrial frequency converter / Appliance / Moto driver medium frequency and high frequency products
2. IH heater / Inductor cooker / Rice cooker / Inverter / Welding / UPS / PFC high frequency products

## Slide 28
Thanks for watching！